## Slide 1: Publication of thesis
09/04-2026
Agenda
Catch up: What was the topic of the thesis? # 10 minutes
  RQs and methods
  Findings and future work ideas
  Recent extended work and findings (since the defense)
Potential article storylines # 15 minutes
  The opportunity cost of electricity sales - navigating offtake contracts in renewable fuel production planning
  Decision support for contracted renewable fuel production - contract structures and risk profiles
  Other?
Target journal/conference # 10 minutes
Planning next meeting # 2 minutes

## Slide 2: Thesis summary
Main RQ
How can long-term contractual offtake commitments be effectively integrated into the daily operational planning of a renewable fuel plant?
Key findings
The opportunity cost of electricity sales under long-term offtake contracts can be accurately estimated using a production-weighted price duration curve.
Day-ahead market participation strategies have been formulated and tested – Obtaining up to 95.3% of optimal profits across a year (with no foresight capabilities).
Obtaining a good estimate of a strike price for the fuel production makes the market participation strategy straightforward and robust against poor short-term forecasting capabilities.
Methods
Rolling horizon optimization
Price duration curves used to identify ópportunity costs.
Bidding strategies: Linear decision rules, stochastic LP-integrated bidding curve identification.

## Slide 3: Case study
Portuguese H2 and NH3 synthesis plant. Large-scale, grid-connected.
Fully linear rolling horizon decision-making model - not modelling inflexible plant units.

## Slide 4: Future work avenues – recent work
How does the methodology handle non-linearity and inflexibility of plant units?
  Keeping the linear model formulation, I model non-linear efficiency curves of the electrolyzer and the ammonia synthesis unit.
What is the dependency on accurate assessment of long-term price trends?
  Instead of simulating the realizations using the DGM, I now also backcast on the 8 years from 2017 to 2024, testing the combined performance of forecast capabilities and decision-making method.
Better alternative strategies other than perfect foresight and fixed hourly production.
  Aggregate model and receding horizon model proposed and tested.

## Slide 5: Non-linear efficiency curves
Chart: Specific electricity consumption
| 10.7 | 15 | 20 | 24.7 | 30 | 40 | 50 | 65 | 100
MWh/t | 4.0278 | 2.9861 | 2.2917 | 1.875 | 1.6389 | 1.3889 | 1.2917 | 1.1806 | 1.1389
Alkaline Electrolyzer
Haber Bosch Unit
Chart: Electricity consumption
| 10.7 | 15 | 20 | 24.7 | 30 | 40 | 50 | 65 | 100
MWh | 0.43097 | 0.44792 | 0.45833 | 0.46313 | 0.49167 | 0.55556 | 0.64583 | 0.76736 | 1.1389

## Slide 6: Non-linear efficiency curves
Alkaline Electrolyzer
Haber Bosch Unit
Chart: Electricity consumption
| 10.7 | 15 | 20 | 24.7 | 30 | 40 | 50 | 65 | 100
MWh | 0.43097 | 0.44792 | 0.45833 | 0.46313 | 0.49167 | 0.55556 | 0.64583 | 0.76736 | 1.1389

## Slide 7: Non-linear efficiency curves - sources
Alkaline Electrolyzer
A conic model for electrolyzer scheduling
Haber Bosch Unit
Heat integration and part-load performance of an SOEC-coupled Haber–Bosch process

## Slide 8: Backcasting
13 month long-term horizon – can be aware of the coming year ahead of time.
Showcases the effects of real market disruptions on the ability to operate optimally.
Preliminary run:

## Slide 9: Better benchmarks
Receding horizon: Make a large model every day including all time steps in the year-ahead problem. Slow put precise.
Aggregate horizon: Create 1 extra time step (after the 96 hour planning horizon) which aggregates the remaining ~8000 hours of flows and trade.
Notes: Computatinal costs: Write solver and algebraic language: (implementation (Pyomo, python)).

## Slide 10: Focus of article
The opportunity cost of electricity sales - navigating offtake contracts in renewable fuel production planning
  Focusing on the ISP methodology.
Decision support for contracted renewable fuel production - contract structures and risk profiles
  Focusing on a decision support framework for identifying “optimal” offtake contract structure.
Other?

## Slide 11: Target journal/conference
Energy Economics
  Maybe most prolific/most difficult.
Applied Energy
  Has published a lot of similar studies.
IAEE Munich
  Opportunity. Abstract deadline tomorrow.

## Slide 12: Next meeting(s)?
Work distribution
Etc.